## Slide 1: Computer Networks Unit II – Physical Layer
Note: Material for this presentations are taken from Internet and books and only being used for student reference

## Slide 2: Outline
Introduction of LAN; MAN;WAN; PAN, Ad-hoc Network
Topologies
Network Architectures OSI Model
TCP/IP Model
Design issues for Layers Transmission Mediums
Network Devices
Manchester and Differential Manchester Encodings;
IEEE802.11: Frequency Hopping (FHSS) and Direct Sequence (DSSS)

## Slide 3: Transmission Mediums
CAT5, 5e, 6
OFC and
Radio Spectrum,

## Slide 4: Common network cable types
Coaxial cable
Unshielded twisted pair
Fiber optic

## Slide 5: UTP characteristics
Unshielded
Twisted (why?) pairs of insulated conductors
Covered by insulating sheath

## Slide 6: UTP categories
Category 1 | Voice only (Telephone)
Category 2 | Data to 4 Mbps (Localtalk)
Category 3 | Data to 10Mbps (Ethernet)
Category 4 | Data to 20Mbps (Token ring)
Category 5 Category 5e | Data to 100Mbps (Fast Ethernet) Data to 1000Mbps (Gigabit Ethernet)
Category 6 | Data to 2500Mbps (Gigabit Ethernet)

## Slide 7: Categories of UTP: CAT 5
100 MHz Bandwidth
24.0 dB Attenuation
100 ohms Impedance
Used for high-speed data transmission
Used in 10BaseT (10 Mbps) Ethernet & Fast Ethernet (100 Mbps)

## Slide 8: Categories of UTP: CAT 5e
150 MHz Bandwidth
24.0 dB Attenuation
100 ohms Impedance
Transmits high-speed data
Used in Fast Ethernet (100 Mbps), Gigabit Ethernet (1000 Mbps) & 155 Mbps ATM
For runs of up to 90 meters
Solid core cable ideal for structural installations (PVC or Plenum)
Stranded cable ideal for patch cables
Terminated with RJ-45 connectors

## Slide 9: Categories of UTP: CAT 6
250 MHz Bandwidth
19.8 dB Attenuation
100 ohms Impedance
Transmits high-speed data
Used in Gigabit Ethernet (1000 Mbps) & 10 Gig Ethernet (10000
Mbps)

## Slide 10: Comparison between CAT5,5e and 6
 | CAT5 | CAT5e | CAT6
Frequency | 100 MHz | 100 MHz | 250 MHz
Attenuation (min. at 100 MHz) | 22 dB | 22 dB | 19.8 dB
Characteristic Impedance | 100 ohms = 15% | 100 ohms = 15% | 100 ohms = 15%
NEXT (min. at 100 MHz) | 32.3 dB | 35.3 dB | 44.3 dB
PS-NEXT (min. at 100 MHz) | NA | 32.3 dB | 42.3 dB
EL-FEXT (min. at 100 MHz) | NA | 23.8 dB | 27.8 dB
PS-ELFEXT (min. at 100 MHz) | NA | 20.8 dB | 24.8 dB
PS-ANEXT (min. at 500 MHz) | -- | -- | --
PS-AELFEXT (min. at 500 MHz) | 16 dB | 20.1 dB | 20.1 dB
Return Loss (min. at 100 MHz) | 16 dB | 20.1 dB | 20.1 dB
Delay Skew (max. per 100m) | NA | 45 ns | 45 ns
Networks Supported | 100BASE-T | 1000BASE-T | 1000BASE-TX

## Slide 11: OFC- Optical fiber cable
An optical fiber cable, also known as fiber optic cable, is an assembly similar to an electrical cable, but containing one or more optical fibers that are used to carry light.
The optical fiber elements are typically individually coated with plastic layers and contained in a protective tube suitable for the environment where the cable will be deployed.
Different types of cable are used for different applications, for example long distance telecommunication, or providing a high-speed data connection between different parts of a building.

## Slide 12: Fiber Media
Optical fibers use light to send information through the optical medium.
It uses the principal of total internal reflection.
Modulated light transmissions are used to transmit the signal.

## Slide 13: Total Internal Reflection

## Slide 14: Fiber Media
Light travels through the optical media by the way of total internal reflection.
Modulation scheme used is intensity modulation.
Two types of Fiber media :
  Multimode
  Singlemode
Multimode Fiber can support less bandwidth than Singlemode Fiber.
Singlemode Fiber has a very small core and carry only one beam of light. It can support Gbps data rates over > 100 Km without using repeaters.

## Slide 15: Single and Multimode Fiber
Single-mode fiber
  Carries light pulses along single path
  Uses Laser Light Source
Multimode fiber
  Many pulses of light generated by LED travel at different angles

## Slide 16: Fiber Media
The bandwidth of the fiber is limited due to the dispersion effect.
Distance Bandwidth product of a fiber is almost a constant.
Fiber optic cables consist of multiple fibers packed inside protective covering.
62.5/125 µm (850/1310 nm) multimode fiber
50/125 µm (850/1310 nm) multimode fiber
10 µm (1310 nm) single-mode fiber

## Slide 17: Fiber-Optic Cable
Contains one or several glass fibers at its core
Surrounding the fibers is a layer called cladding

## Slide 18: Fiber Optic Cable
FO Cable may have 1 to over 1000 fibers

## Slide 19: Radio Spectrum
The radio spectrum is the part of the electromagnetic spectrum from 3 Hz to 3000 GHz (3 THz).
Electromagnetic waves in this frequency range, called radio waves, are extremely widely used in modern technology, particularly in telecommunication.
Coordinated by an international body, the International Telecommunication Union (ITU)

## Slide 20: Frequency Band

## Slide 21: Outline
Introduction of LAN; MAN;WAN; PAN, Ad-hoc Network
Topologies
Network Architectures OSI Model
TCP/IP Model
Design issues for Layers
Transmission Mediums Network Devices
Manchester and Differential Manchester Encodings;
IEEE802.11: Frequency Hopping (FHSS) and Direct Sequence (DSSS)

## Slide 22: Devices and the layers at which they operate
Layer | Name of Layer | Device
3 | Network | Routers, layer 3 switches
2 | Data Link | Switches, bridges, NIC’s
1 | Physical | Hubs, Repeaters

## Slide 23: Network Devices:
Bridge
Switch
Router
Brouter and
Access Point

## Slide 24: Hubs
A hub is used as a central point of connection among media segments.
Cables from network devices plug in to the ports on the hub.
Types of HUBS :
  A passive hub is just a connector. It connects the wires
coming from different branches.
  The signal pass through a passive hub without regeneration or amplification.
  Connect several networking cables together
  Active hubs or Multiport repeaters- They regenerate or amplify the signal before they are retransmitted.

## Slide 25: Repeaters
A repeater is a device that PHYSICAL layer.
operates only at the
A repeater can be used to increase the length of the network by eliminating the effect of attenuation on the signal.
It connects two segments of the same network, overcoming the distance limitations of the transmission media.
A repeater forwards every frame it has no filtering capability.
A repeater is a regenerator, not an amplifier.
Repeaters can connect segments that have the same access method. (CSMA/CD, Token Passing, Polling, etc.)
Optic fiber repeater

## Slide 26
Rep
eater connecting two segments of a LAN
Function of a repeater

## Slide 27: Switches
A network switch is a computer networking device that connects devices together on a computer network by using packet switching to receive, process, and forward data to the destination device.
Unlike less advanced network hubs, a network switch forwards data only to the devices that need to receive it, rather than broadcasting the same data out of each of its ports.
It uses Ethernet (MAC Address) address.

## Slide 28: Store and Forward Switches
Do error checking on each frame after the entire frame has arrived into the switch
If the error checking algorithm determines there is no error, the switch looks in its MAC address table for the port to which to forward the destination device
Highly reliable because doesn’t forward bad frames
Slower than other types of switches because it holds on to each frame until it is completely received to check for errors before forwarding

## Slide 29: Cut Through Switch
Faster than store and forward because doesn’t perform error checking on frames
Reads address information for each frame as the frames enter the switch
After looking up the port of the destination device, frame is forwarded
Forwards bad frames
  Performance penalty because bad frames can’t be used and replacement frames must be sent which creates additional traffic

## Slide 30: Unmanaged/Intelligent switches
Unmanaged – provides LAN’s with all the benefits of switching. Fine in small networks
Intelligent switches tracks and reports LAN performance statistics. Have a database ASIC (application specific integrated circuit) on board to collect and store data which you view through a software interface

## Slide 31: Comparison of Hub and Switch
Basis for Comparison | Hub | Switch
Layer | Physical layer. Layer 1 devices | Data Link Layer. Layer 2
Function | To connect a network of personal computers together, they can be joined through a central hub. | Allow to connect multiple device and port can be manage,Vlan can create security also can apply
Data Transmission | Electrical signal or bits | Frame (L2 Switch) Frame & Packet (L3 switch)
Ports | 4/12 ports | Switch is multi port Bridge. 24/48 ports
Device Type | Passive Device (Without Software) | Active Device (With Software) & Networking device
Used in | LAN | LAN
Transmission Mode | Half duplex | Half/Full duplex
Broadcast Domain | Hub has one Broadcast Domain. | Switch has one broadcast domain
Definition | An electronic device that connects many network device together so that devices can exchange data | A network switch is a computer networking device that is used to connect many devices together on a computer network. A switch is considered more advanced than a hub because a switch will on send msg to device that needs or request it
Speed | 10Mbps | 10/100 Mbps, 1 Gbps
Collisions | Collisions occur in setups using hubs. | No collisions occur in a full-duplex switch.
Address Used | Uses MAC address | Uses MAC address

## Slide 32: Bridges
Operates in both the PHYSICAL and the data linklayer.
As a
PHYSICAL layer device, it regenerates
the signal
it receives.
As a data link layer device, the
bridge can check
the PHYSICAL/MAC addresses(source and destination) contained in the frame.
A bridge has a table used in filtering decisions.
It can check the destination address of a frame and decide if the frame should be forwarded or dropped.
If the frame is to be forwarded, the decision mustspecify the port.
A bridge has a table that maps address to ports.
Limit or filter traffic keeping local traffic local yet allow connectivity to other parts (segments).

## Slide 33
A bridge connecting two LANs
A bridge does not change the physical (MAC) addresses in a frame.

## Slide 34: How BridgesWork
Bridges work at the Media Access Control
Routing table is built to record the segment no. of address
If destination address is in the same segment as the source address, stop transmit
Otherwise, forward to the other segment

## Slide 35: Characteristics of Bridges
Contains one entry per station of network to which bridge is
connected.
Is used to determine the network of destination station of a received packet.
Routing Tables
Is used by bridge to allow only those packets destined to the remote network.
Packets are filtered with respect to their destination and multicast addresses.
Filtering
the process of passing a packet from one network to another.
Forwarding
the process by which the bridge learns how to reach stations on the internetwork.
Learning Algorithm

## Slide 36: Types of Bridges
Transparent Bridge
Also called learning bridges
Build a table of MAC addresses as frames arrive
Ethernet networks use transparent bridge
Duties of transparent bridge are : Filtering frames,
forwarding and blocking
Source Routing Bridge
Used in Token Ring networks
Each station should determine the route to the destination when it wants to send a frame and therefore include the route information in the header of frame.
Addresses of these bridges are included in the frame.
Frame contains not only the source and destination address but also
the bridge addresses.

## Slide 37: Advantages And Disadvantages Of Bridges
Advantages of using a bridge
  Extend physical network
  Reduce network traffic with minor segmentation
  Creates separate collision domains
  Reduce collisions
  Connect different architecture
Disadvantages of using bridges
  Slower that repeaters due to filtering
  Do not filter broadcasts
  More expensive than repeaters

## Slide 38: Comparison of Switch and Bridge
Switch | Bridge
A switch when compared to bridge has multiple ports. Switches can perform error checking before forwarding data. Switches are very efficient by not forwarding packets that error-ed out or forwarding good packets selectively to correct devices only. Switches can support both layer 2 (based on MAC Address) and layer 3 (Based on IP address) depending on the type of switch. Usually large networks use switches instead of hubs to connect computers within the same subnet. | Bridge has a single incoming and outgoing port. A bridge maintains a MAC address table for both LAN segments it is connected to. Bridge filters traffic on the LAN by looking at the MAC address. Bridge looks at the destination of the packet before forwarding unlike a hub. It restricts transmission on other LAN segment if destination is not found. Bridges are used to separate parts of a network that do not need to communicate regularly, but need to be connected.

## Slide 39: Two and Three layer switches
Two layer switch operate at PHY and data link layer
Three layer switch operates at network layer
Bridge is an example of two-layer switch.
Bridge with few port can connect a few LANs
Bridge with many port may be able to allocate a unique port to each station, with each station on its own independent entity.This means no competing traffic (no collision as we saw in Ethernet)

## Slide 40: 3-layer switches- Router
Routes packets based on their logical addresses (host-to-host addressing)
A router normally connects LANs and WANs in the Internet and has a routing table that is used for making decision about the route.
The routing tables are normally dynamic and are updated using routing protocols.
Routers connecting independent LANs and WANs

## Slide 41: Advantages and Disadvantages of Routers
Advantages
  Routers
-provide sophisticated routing, flow control, and traffic isolation
-are configurable, which allows network manager to make policy based on routing decisions
-allow active loops so that redundant paths are available
Disadvantages
  Routers
  are protocol-dependent devices that must understand the protocol they are forwarding.
  can require a considerable amount of initial
configuration.
  are relatively complex devices, and generally are more expensive than bridges.

## Slide 42: Routers versus Bridges
Addressing
  Routers are explicitly addressed.
  Bridges are not addressed.
Availability
  Routers can handle failures in links, stations, and other routers.
  Bridges use only source and destination MAC address, which does not guarantee delivery of frames.
Message Size
» Routers can perform fragmentation on packets and thus handle different packet sizes.
» Bridges cannot do fragmentation and should not forwarda frame which is too big for the next LAN.
Forwarding
» Routers forward a message to a specific destination.
» Bridges forward a message to an outgoing network.

## Slide 43
Priority
» Routers can treat packets according to priorities
» Bridges treat all packets equally.
Error Rate
» Network layers have error-checking algorithms that examines each received packet.
provides a very low undetected bit error
» The MAC layer rate.
Security
» Both bridges and routers provide the ability to put “security walls” around specific stations.
» Routers generally provide greater security than bridges because
they can be addressed directly and
they use additional data for implementing security.

## Slide 44: Brouters: Bridging Routers
Combine features of bridges and routers.
Capable of establishing a bridge between two networks as well as routing some messages from the bridge networks to other networks.
Are sometimes called (Layer 2/3) switches and are a combination of bridge/router hardware and software.

## Slide 45: Gateway
Interchangeably used term router and gateway
Connect two networks above the network layer of OSI model.
Are capable of converting data frames and network
protocols into the format needed by another network.
Provide for translation services between different computer protocols.
Transport gateways make a connection between two networks at the transport layer.
Application gateways connect two parts of an application in the application layer, e.g., sending email between two machines using different mail formats
Broadband-modem-router is one e.g. of gateway

## Slide 46: Access Point
In computer networking, a wireless access point (WAP) is a networking hardware device that allows a Wi-Fi device to connect to a wired network.The WAP usually connects to a router (via a wired network) as a standalone device, but it can also be an integral component of the router itself.

## Slide 47: Access Point
Access Point(AP) units serve areas of a building, similar to base units of cordless telephones except each AP can connect to many computers. APs serve as network bridges between the wired and wireless portions of the network.

## Slide 48: Outline
Introduction of LAN; MAN;WAN; PAN, Ad-hoc Network
Topologies
Network Architectures OSI Model
TCP/IP Model
Design issues for Layers
Transmission Mediums Network Devices
Manchester and Differential Manchester Encodings;
IEEE802.11: Frequency Hopping (FHSS) and Direct Sequence (DSSS)

## Slide 49: Encoding
Coding is the process of embedding clocks into a given data stream and
producing a signal that can be transmitted over a selected medium.
Transmitter is responsible for "encoding" i.e. inserting clocks into data according to a selected coding scheme
Receiver is responsible for "decoding" i.e. separating clocks and data from the incoming embedded stream.
A signal needs to be manipulated in such a way so that it contains identifiable changes that are recognizable to the sender and receiver.
There are 4 possible encoding techniques that can be used on the data: Digital- to-digital, Digital-to-Analog, Analog-to-analog, Analog-to-digital.

## Slide 50: Digital-to-Digital Encoding
The binary signals created by your computer (DTE) are translated into a sequence of voltage
pulses that can be sent through the transmission medium.
Binary signals have two basic parameters: amplitude and duration.
As the number of bits sent per unit of time increases, the bit duration decreases.
The three most common methods of encoding used are: unipolar , polar , and bipolar .

## Slide 51: UNIPOLAR ENCODING
Unipolar encoding uses only one voltage level.

## Slide 52: Lack of synchronization

## Slide 53: POLAR ENCODING
Polar encoding uses two voltage levels (positive and negative).

## Slide 54: Manchester
(or diphase or biphase encoding)
This code is self-clocking.
Provides a transition for every bit in the middle of the bit cell. This transition is used only to provide clocking.
+ve to -ve transition for a "0" bit
-ve to +ve transition for a "1" bit
Residual DC component is eliminated by having both polarities for every bit.
This scheme is used in Ethernet and IEEE 802.3 compliant LANs

## Slide 55: Manchester Encoding
In Manchester encoding, the transition at the middle of the bit is used for both synchronization and bit representation.

## Slide 56: Differential Manchester Coding
Code is self-clocking
Transition for every bit in the middle of the bit cell
Transition at the beginning of the bit cell if the next bit is " 0 "
NO Transition at the beginning of the bit cell if the next bit is " 1 "
Used in Token Ring or IEEE 802.5-compliant LANs.

## Slide 57: Differential Manchester encoding
In differential Manchester encoding, the transition at the middle of the bit is used only for synchronization.
The bit representation is defined by the inversion or noninversion at the beginning of the bit.

## Slide 58: Outline
Introduction of LAN; MAN;WAN; PAN, Ad-hoc Network
Topologies
Network Architectures OSI Model
TCP/IP Model
Design issues for Layers
Transmission Mediums Network Devices
Manchester and Differential Manchester Encodings;
IEEE802.11: Frequency Hopping (FHSS) and Direct Sequence (DSSS)

## Slide 59: IEEE 802 Standards
158
The important ones are marked with *. The ones marked with  are hibernating. The
one marked with † gave up.

## Slide 60: IEEE developed the first internationally recognized wireless LAN standard – IEEE 802.11 in 1997
IEEE 802.11 Wireless LAN Standard
Scope of IEEE 802.11 is limited to
Physical and Data Link Layers.

## Slide 61: IEEE 802.11 Standards
802.11a (OFDM Waveform)
802.11b
802.11g
802.11n
802.11ac
802.11ad
802.11af
802.11ah
802.11ai
802.11aj
802.11aq
802.11ax

## Slide 62: Physical Media of 802.11 Standard
Operating in 2.4 GHz ISM band
Lower cost, power consumption
Most tolerant to signal interference
Operating in 2.4 GHz ISM band
Supports higher data rates
More range than FH or IR physical layers
Frequency- hopping spread spectrum
Direct-sequence spread spectrum
Lowest cost
Lowest range compared to spread spectrum
Doesn’t penetrate walls, so no eavesdropping
Infrared

## Slide 63: What is meant by Spread Spectrum
Spread spectrum is a form of wireless communications in which the frequency of the transmitted signal is varied.This results in a much greater bandwidth than the signal (Bss >> B)
This technique decreases the potential interference to other receivers while achieving privacy.
Two types of Spread Spectrum- FHSS and DSSS

## Slide 64: Spread spectrum

## Slide 65: Frequency Hopping Spread Spectrum (FHSS)
Signal is broadcast over seemingly random series of radio frequencies
Signal hops from frequency to frequency at fixed intervals
Receiver, hopping between frequencies in synchronization with transmitter, picks up message
Advantages
Efficient utilization of available bandwidth Eavesdropper hear only unintelligible blips
Attempts to jam signal on one frequency succeed only at knocking out a few bits

## Slide 66: Frequency hopping spread spectrum (FHSS)

## Slide 67: Frequency hopping spread spectrum (FHSS)

## Slide 68: FHSS cycles

## Slide 69: Bandwidth sharing difference between FDM and FHSS

## Slide 70: Direct Sequence Spread Spectrum (DSSS)
Each bit in original signal is represented by multiple bits in the transmitted signal
Spreading code spreads signal across a wider frequency band
DSSS is the only physical layer specified for the 802.11b specification
802.11a and 802.11b differ in use of chipping method 802.11a uses 11-bit barker chip
802.11b uses 8-bit complimentary code keying (CCK) algorithm

## Slide 71: Direct Sequence Spread Spectrum (DSSS)

## Slide 72: DSSS example

## Slide 73: FHSS Vs DSSS
FH systems use a radio carrier that “hops” from frequency to frequency in a pattern known to both transmitter and receiver
  Easy to implement
  Resistance to noise
  Limited throughput (2-3 Mbps @ 2.4 GHz)
DS systems use a carrier that remains fixed to a specific frequency band.The data signal is spread onto a much larger range of frequencies (at a much lower power level) using a specific encoding scheme.
  Much higher throughput than FH (11 Mbps)
  Better range
  Less resistant to noise (made up for by redundancy – it transmits at least 10 fully redundant copies of the original signal at the same time)

## Slide 74: Outline
Introduction of LAN; MAN;WAN; PAN, Ad-hoc Network
Topologies
Network Architectures OSI Model
TCP/IP Model
Design issues for Layers
Transmission Mediums Network Devices
Manchester and Differential Manchester Encodings;
IEEE802.11: Frequency Hopping (FHSS) and Direct Sequence (DSSS)

## Slide 75: References
Websites:
http://www.studytonight.com/computer-networks/
https://cs.fit.edu/~pkc/classes/dc/slides/ch3.ppt
https://www.techopedia.com/2/29090/networks/lanwanman-an-overview-of-network-types
https://www.slideshare.net/ENGMSHARI/adhoc-networks
http://www.businessdictionary.com/definition/distributed-network-architecture-DNA.html
https://en.wikipedia.org/wiki/Optical_fiber_cable
https://en.wikipedia.org/wiki/Radio_spectrum
https://www.slideshare.net/rupinderj/networking-devices-12807479
https://en.wikipedia.org/wiki/Wireless_access_point
https://www.slideshare.net/LukaXavi/data-encoding
Text Books:
Andrew S.Tenenbaum, “Computer Networks”,5th Edition, PHI, ISBN 81-203-2175-8.
Fourauzan B., "Data Communications and Networking", 5th Edition, Tata McGraw- Hill, Publications, 2006